## Slide 1
EI Fragment
Exact-Mass Calculator
Automated identification of fragment ion formulas
from unit-mass EI spectra
v1.1.0 · Pure Python · Zero Dependencies · 49 Tests

## Slide 2
The Challenge
EI Mass Spectrometry
Unit-mass resolution: peaks at integer m/z only
Molecular ion M+• loses one electron: Δm = 0.000549 Da
Each fragment peak may have multiple possible formulas
Manual formula assignment is tedious and error-prone
Unit Mass
Integer m/z peaks
Fragment Ions
Smaller than M+•
Formula Ambiguity
Multiple candidates per peak
Goal
All valid exact-mass candidates, ranked

## Slide 3
Workflow Overview — Processing Pipeline
① SDF Input Molecular formula + EI spectral peaks
② Parse Formula Elements loaded from elements.csv
③ For Each Peak Iterate nominal m/z values
④ Enumerate Candidates Cartesian product of element counts
⑤ Apply Filters Mass window · DBE · Electron correction
⑥ Isotope Patterns Polynomial convolution (optional)
⑦ Output Ranked formulas with exact masses

## Slide 4
Fragment Enumeration — Constrained Cartesian-Product Algorithm
Parent Formula as UPPER BOUND
A fragment can never contain more atoms of any element than the intact molecule — conservation of mass and atoms.
Why this matters:
Avoids generating impossible formulas (e.g. C₁₅ from a C₁₀ parent), reducing the search space drastically.
C₁₀H₁₂O₂ → C: 0–10 · H: 0–12 · O: 0–2
Works for ALL fragment sizes — from m/z 1 to M+•
Molecule | Combinations | Time
C₁₀H₁₂O₂ | 429 | < 1 ms
C₂₀H₂₅NO₃ | 4,368 | ~5 ms
C₃₀H₅₀N₂O₅S | ~10⁷ | ~2 s

## Slide 5
Filters — Three-Stage Filtering
① Mass Window
|ion_m/z − nominal_mz| ≤ tolerance
Default: ±0.5 Da
Accepts all formulas that round to the correct nominal mass
② Electron Correction
remove: ion = M − mₙ (EI+ default)
add: ion = M + mₙ (EI−)
none: ion = M
mₙ = 0.000 548 58 Da
③ DBE Check
DBE = 1 + C − H/2 + N/2 − halogens/2
DBE < 0 → impossible
DBE = integer → even-electron
DBE = half-int → radical cation (M+•)

## Slide 6
Isotope Patterns — Theoretical Isotope Simulation
Polynomial Convolution Method
Step 1: Start: { mass = 0, abundance = 1.0 }
Step 2: For each atom: convolve with element isotopes from CSV
Step 3: Prune peaks < 0.1% relative abundance
Step 4: Normalise to 100% (most abundant peak)
CSV-driven: update elements.csv to change isotope abundances
Example: C₆H₆ (Benzene)
Peak | Mass (Da) | Rel. Abundance
M (C₆H₆) | 78.04695 | 100.0 %
M+1 | 79.05031 | 6.6 %
M+2 | 80.05368 | 0.2 %
Why convolution?
Each element contributes its isotope distribution independently. Convolution combines them exactly — no approximations needed.

## Slide 7
CSV Element Database — elements.csv: Single Source of Truth
Design Principles
All element data lives in one CSV file
No hardcoded constants in Python source
Easily extended with new elements
Columns:
Symbol · Name · Isotope · ExactMass
Abundance · Valence · MonoisotopicFlag
Symbol | Isotope | ExactMass | Abundance | Valence
H | 1 | 1.007825 | 0.99989 | 1
H | 2 | 2.014102 | 0.00011 | 1
C | 12 | 12.000000 | 0.98930 | 4
C | 13 | 13.003355 | 0.01070 | 4
Cl | 35 | 34.968853 | 0.75760 | 1
Cl | 37 | 36.965903 | 0.24240 | 1

## Slide 8
Usage & Installation — Quick Start
Install
git clone https://github.com/your-org/ei-fragment-calculator
cd ei-fragment-calculator
pip install -e .
CLI Options
Flag | Default | Description
--electron remove/add/none | remove | Electron-mass correction mode
--tolerance 0.5 | 0.5 Da | Mass window
--isotope | off | Show isotope patterns
--output FILE | stdout | Save results to file
--hide-empty | off | Hide peaks with no candidates
ei-fragment-calc spectra.sdf --isotope --electron remove --output results.txt